## Slide 1: Rethinking Global Routing: Congestion Reduction and Multiobjective Optimization
Hamid Shojaei
Department of Electrical and Computer Engineering
University of Wisconsin, Madison
WISCAD VLSI Design Automation Lab http://wiscad.ece.wisc.edu
PhD Defense Exam on 05/21/2012

## Slide 2: Outline
Introduction
CGRIP
  A framework for routing congestion analysis
LCGRIP
  Planning for local congestion in global routing
Summary of contributions
Conclusions
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 3: Standard Global Routing
Objectives of standard global routing
  Serves as a critical step after placement
  Provides coarse routes for detailed routing
  Provides congestion map for placement
Placement
Global Routing
Detailed Routing
Partitioning
Floorplanning
Timing Closure
GR
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 4: Standard Global Routing
C3
n1
n4
n5
n3
C1
n1
n2
n1
n5
C2
n5
n3
n4
n2
C3
n1
n4
n5
n3
C1
n1
n2
n1
n5
C2
n5
n3
n4
n2
Design after Placement
Design after Global Routing
Design after Detailed Routing
Introduction
Conclusions
CGRIP
LCGRIP
Summary
C3
n1
n4
n5
n3
C1
n1
n2
n1
n5
C2
n5
n3
n4
n2

## Slide 5: Global Routing Grid Graph
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
C3
n1
n4
n5
n3
C1
n1
n2
n1
n5
C2
n5
n3
n4
n2
Introduction
Conclusions
CGRIP
LCGRIP
Summary
Vias

## Slide 6: Global Routing Grid Graph
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
C3
n1
n4
n5
n3
C1
n1
n2
n1
n5
C2
n5
n3
n4
n2
Routes are trees on the grid graph
  Local nets (e.g. n4) are ignored
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 7: Global Routing Grid Graph
Horizontal global cell
αi
αi+2
αi+1
βi
βi+2
βi+1
Vertical global cell
edge capacity
edge capacity
normalized capacity:
edge utilization: = # of wires that pass edge
normalized overflow
actual overflow:
Overflow!!
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 8: Rethinking Global Routing
Placement
Congestion Analysis for Modern Designs
CGRIP
Multi-objective
Global Routing
Coll-MGR
Detailed Routing
Congestion-aware
Global Routing
LCGRIP
Other Global Routers
Standard Flow
Proposed Flow
Placement
Global Routing
Detailed Routing
Covered in prelim exam
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 9
CGRIP: A Framework for Routing Congestion Analysis
in Modern Designs
Placement
Congestion Analysis for Modern Designs
CGRIP
Multi-objective
Global Routing
Coll-MGR
Detailed Routing
Congestion-aware
Global Routing
LCGRIP
Other Global Routers

## Slide 10: Goals of Congestion Analysis
Captures factors that contribute to congestion in modern design
  Variations in wire size and spacing at different metal layers
  Virtual pins located at the higher metal layers
  Routing blockages, reserved for embedded IPs and memories
Requires handling a flexible model of global routing
(Alpert et al. DAC2010)
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 11: Goals of Congestion Analysis
Creates an accurate congestion map
  Accurately identifies the locations of the congested “regions” on the layout and the amount of congestion at each location
Runs fast to allow iterative calls when integrated within the design flow, e.g., with routability-driven placement
Routability-driven Placement
Congestion
Analysis
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 12: Contributions
An Integer Programming (IP) formulation expressing “the congestion analysis problem”
  Allows finding the locations of the congested regions using a resolution parameter
New ideas for a practical realization of the IP
  Reduced-sized Linear Programming (RLP)
  Multiple Ripup Single Re-route (MRSR)
  Congestion-aware Minimum Spanning Tree for multi-terminal net deomposition (CMST)
  Congestion-aware Layer Assignment (CLA)
CGRIP: congestion analysis tool
  Stable, fast, flexible router, handling complicating factors
    Simpler variation, coalesCgrip, judged the ISPD 2011 contest
  Released at http://wiscad.ece.wisc.edu/gr/cgrip
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 13: Motivational Example
To quickly obtain an accurate congestion map, what is an effective optimization objective?
  Example: ran different variations of CGRIP on a placement of superblue2
    Case (a) minimizes TOF in a short time i.e., 15 minutes
    Case (b) regionally minimizes overflow in a short time, 15 minutes on 100 regions
    Case (c) minimizes TOF in a long time, i.e., 60 minutes
  Maps (a) and (b) have similar TOF, however map (b) is more accurately matching (c) in terms of the locations of highly-utilized edges on the GR grid-graph
(a) TOF=329K
(b) TOF=330K
(c) TOF=64K (reference)
(c) TOF=64K
15min
15min
60min
(reference)
Introduction
Conclusions
CGRIP
LCGRIP
Summary
Notes: For each map only edges with a utilization higher than 70% is shown

## Slide 14: Motivational Example
To quickly obtain an accurate congestion map, what is an effective optimization objective?
  Minimizing TOF is NOT a good objective within a short runtime budget
  Router prioritizes different regions based on its ripup and re-route procedure, typically to get maximum reduction in TOF
  May not have the chance to optimize some regions in a short run but this is not an indication of unroutability since the same router could fix these regions for a longer run
(a) TOF=329K
(b) TOF=330K
(c) TOF=64K (reference)
(c) TOF=64K
15min
15min
60min
(reference)
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 15: Defining Regions
Two input resolution parameters control the size and the number of regions
For a small time-budget
  Resolution is set to be much lower than the global routing grid
    Identification of the congestion regions is with respect to the granularity defined by the regions rather than each edge of the GR grid-graph and thus can be done more accurately
ry=2
rx =3
# regions = 6
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 16: Overlapping Regions
In (a) r1-r4 are equally ranked in terms of congestion
  The location of the congested region is not identified accurately
Adding the overlapping region r5 in (b) allows capturing the location of the congested region more accurately
(a)
(b)
r1
r2
r3
r4
r1
r2
r3
r4
r5
(c)
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 17: IP-CA: An IP for Congestion Analysis
S1
T1
S2
T2
o10
o1
o2
o3
o4
o5
o6
o7
total overflow at each region
maximum overflow at each region
Special case: k=0 and |R|=|E|
qr=oe
Formulation minimizes TOF (GRIP [TCAD’11])
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 18: CGRIP: Framework Overview
Solving IP-CA directly is impractical
  Large problem size with binary variables
Our solution for realizing a fast procedure
  Solve a reduced-sized and relaxed version of IP-CA as a Reduced Linear Program (RLP)
  Effectively integrate RLP in a standard ripup and re-route framework
    Both INIT and RRR steps evoke RLP
    Other new features added to the standard ripup and re-route framework
      Accounting for wire size and spacing and virtual pins for each metal layer in 2D projection and CLA steps
2D projection
Initial solution (INIT)
(evokes RLP)
Ripup and re-route (RRR)
(evokes RLP)
Congestion-aware Layer Assignment (CLA)
Terminate?
No
Yes
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 19: CGRIP: 2D Projection
Computing normalized capacity of an edge in the projected 2D graph
  The normalized capacity of a 2D edge is summation of normalized capacities of corresponding edges in the 3D graph
  Accounts for routing blockages
b=1
b=2
b=3
Introduction
Conclusions
CGRIP
LCGRIP
Summary
1x
2x

## Slide 20: CGRIP: Framework Overview
Solving IP-CA directly is impractical
  Large problem size with binary variables
Our solution for realizing a fast procedure
  Solve a reduced-sized and relaxed version of IP-CA as a Reduced Linear Program (RLP)
  Effectively integrate RLP in a standard ripup and re-route framework
    Both INIT and RRR steps evoke RLP
    Other new features added to the standard ripup and re-route framework
      Accounting for wire size and spacing and virtual pins for each metal layer in 2D projection and CLA steps
2D projection
Initial solution (INIT)
(evokes RLP)
Ripup and re-route (RRR)
(evokes RLP)
Congestion-aware Layer Assignment (CLA)
Terminate?
No
Yes
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 21: RLP: Overview
A small set of candidate routes per net
Previous congestion map
Regions defined by the resolution parameter
Updated congestion map
A new routing solution per net
RLP: A reduced version of IP-CA with a subset of relaxed variables, generates an approximate solution in minutes
inputs
outputs
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 22: RLP: Procedure
Budget regions for critical edges
Select critical edges
Adjust edge capacities for the impact of the remaining nets
Select critical nets & up to 10 candidate routes per selected net
Utilization of the critical edges from dual values
Route for all the nets
Utilization of all the edges
greedy heuristic
critical nets and edges
Solve RLP: the reduced and relaxed IP-CA
Route for the critical nets
Introduction
Conclusions
CGRIP
LCGRIP
Summary
and are set to be 5k and 1k

## Slide 23: INIT: Procedure
Decompose multi-terminal nets into two-terminal subnets
Solve RLP to generate initial solution
Maze routing (1)
RLP
candidate routes
used to approximate congestion to identify critical nets and edges
Pattern routing (4)
2D projection
Initial solution (INIT)
(evokes RLP)
Ripup and re-route (RRR)
(evokes RLP)
Congestion-aware Layer Assignment (CLA)
Terminate?
No
Yes
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 24: RRR: Procedure
Update edge utilization
(evokes RLP)
Order decomposed nets
MRSR
SRSR
Improved overflow
by MRSR
in previous RRR
?
Improved overflow
by SRSR?
CMST
yes
no
no
Introduction
Conclusions
CGRIP
LCGRIP
Summary
Multiple Ripup
Single Re-route
Congestion-aware Minimum
Spanning Tree
for net decomposition
Order decomposed nets
SRSR
Single Ripup Single Re-route
Standard RRR
Proposed RRR

## Slide 25: Multiple Ripup Single Re-route
Subnets of different nets often have the terminals mapping to the same vertices in the GR grid graph
  In the first step of RRR for benchmark superblue1, 595K nets out of 1409K can be removed by MRSR
G1:
P1
P2
3
G2:
P1
P2
1
G3:
P1
P3
2
n1
n2
n3
n6
n4
n5
# of sub-nets = 6
Average edge capacity = 3
Utilization Factor
p1
p2
p3
p1
p2
p3
n1
n2
n4
n3
n5
n6
G2
G1
G3
,
,,
,
,
,
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 26: Congestion-aware Net Decomposition
Standard MST
Congestion-aware MST
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 27: CGRIP: Layer Assignment
Removes overlap between subnets
For each net assigns 2D edges into 3D
Maze routing procedure
  Minimizes wirelength and overflow
  Accounts for
    Varying wire sizes and spacing
    Virtual pins located on higher layers
    Routing blockages
2D projection
Initial solution (INIT)
(evokes RLP)
Ripup and re-route (RRR)
(evokes RLP)
Congestion-aware Layer Assignment (CLA)
Terminate?
No
Yes
Introduction
Conclusions
CGRIP
LCGRIP
Summary
Notes: Hamid this is unclear. Do you have one 3 terminal net in this figure? Your sentence “Steiner point … are identified” is unclear

## Slide 28: About coalesCgrip
The variation of CGRIP used to judge the ISPD 2011 contest on routability-driven placement
  Uses FGR [TCAD’08] to generate an initial solution (INIT step)
  Runs a simpler variation of CGRIP after initial solution
    Maximum resolution
    Uses RLP but for IP-CA which minimizes the total overflow
    Does not have the MRSR and CMST steps
    Uses a greedy approach for layer assignment
Introduction
Conclusions
CGRIP
LCGRIP
Summary
coalesCgrip
CGRIP

## Slide 29: Simulation Setup
Both coalesCgrip and CGRIP support the new bookshelf format used in the ISPD 2011 benchmark suites
  Has different wire sizes and spacings for 9 metal layers
  Non-rectangular cells and routing obstacles
  Virtual pins located at the higher metal layers
Design | Nodes | Terminals | Terminal_NI | Nets | X x Y
superblue1 | 847441 | 52627 | 29712 | 822744 | 704x516
superblue2 | 1014029 | 59312 | 33444 | 990899 | 770x1114
superblue4 | 600220 | 40550 | 38204 | 567607 | 467x415
superblue5 | 772457 | 74365 | 20676 | 786999 | 774x713
superblue10 | 1129144 | 153595 | 60628 | 1085737 | 638x968
superblue12 | 1293433 | 8953 | 6396 | 1293436 | 444x518
superblue15 | 1123963 | 252053 | 42296 | 1080409 | 399x495
superblue18 | 483452 | 25063 | 15984 | 468918 | 381x404
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 30: 1) Minimizing Total Overflow (TOF)
Design | Placer | coalesCgrip |  | CGRIP |  | 
 |  | TOF | WL | TOF | WL | TOF Imp.%
superblue1 | SimPLR | 0 | 150.24 | 0 | 151.14 | 0.00
superblue2 | Ripple | 797898 | 307.73 | 115332 | 330.14 | 85.55
superblue4 | Ripple | 85538 | 108.57 | 1414 | 114.38 | 98.35
superblue5 | Ripple | 126186 | 172.86 | 20252 | 180.56 | 83.95
superblue10 | RADIANT | 616742 | 250.16 | 59306 | 267.84 | 90.38
superblue12 | SimPLR | 415428 | 228.85 | 35298 | 243.16 | 91.50
superblue15 | Ripple | 125936 | 179.11 | 12832 | 192.17 | 89.81
superblue18 | mPL11 | 31440 | 98.44 | 0 | 104.34 | 100.00
Took placement instances from the ISPD 2011 contest website
Used maximum resolution in CGRIP to minimize TOF
15 minutes runtime budget for both coalesCgrip and CGRIP
TOF is improved by 80% compared to coalesCgrip
Introduction
Conclusions
CGRIP
LCGRIP
Summary
* WL should be scaled up to 10^5

## Slide 31: 1) Impact of Features in CGRIP
Compared to CGRIP-all
  CMST, MRSR, and RLP on average can improve OF by 49%, 51%, and 63%
  CGRIP+all in average improves OF by 78%
% overflow Improvement
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 32: 2) Ranking the Congested Regions
Ran CGRIP in three modes:
  maxRes60: minimizing TOF with a time budget of 60 minutes
  maxRes15: minimizing TOF with a time-budget of 15 minutes
  lowRes15: regional minimization of overflow for rxxry=10x10 regions with a time-budget of 15 minutes and in two modes:
    NOV: no overlap between regions
    OV: overlap between regions
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 33: 2) Ranking the Congested Regions
Evaluated the solution of each case by:
  Imposing a 10x10 resolution and ranking the resulting regions based on descending overflow in each case
  Took maxRes60 as reference
    Identified critical regions Rc with non-zero overflow and their ranks
  Evaluated the accuracy of maxRes15 and lowRes15 by this metric
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 34: 2) Ranking the Congested Regions
lowRes15 always provides a better ranking than maxRes15
OV always provides a better ranking than NOV
% Err for NOV
% Err for OV
Chart: 
| superblue1 | superblue2 | superblue4 | superblue5 | superblue10 | superblue12 | superblue15 | superblue18 | average
maxRes15 | 0 | 27.43 | 26.95 | 36.2 | 66.67 | 25.53 | 54.5 | 58.05 | 36.9162
lowRes15 | 0 | 8.12 | 10.02 | 15.12 | 31.39 | 8.18 | 28.46 | 20.37 | 15.2075
Chart: 
| superblue1 | superblue2 | superblue4 | superblue5 | superblue10 | superblue12 | superblue15 | superblue18 | average
maxRes15 | 0 | 13.43 | 13.85 | 16.18 | 35.69 | 12.38 | 36.2 | 27.47 | 19.4
lowRes15 | 0 | 2.02 | 9.8 | 10.4 | 22.78 | 7.12 | 21.09 | 14.2 | 10.9262
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 35
LCGRIP: Planning for Local Net Congestion
in Global Routing
Placement
Congestion Analysis for Modern Designs
CGRIP
Multi-objective
Global Routing
Coll-MGR
Detailed Routing
Congestion-aware
Global Routing
LCGRIP
Other Routers

## Slide 36: Congestion Impact of Local Nets
Modern designs have high pin density translating to high number of local nets
  In ISPD11 benchmarks, 31.20% of nets are local
Local nets consume wire track and block access to pins
Local nets are ignored in standard global routing
They can cause serious routability issues at the detailed routing stage
It is desirable to have a global router that comprehensively
accounts for congestion impact of local nets
in addition to the previously-mentioned factors
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 37: LCGRIP: Contributions
To deal with local nets
  A procedure to generate non-uniform global cells to reduce the number of local nets while keeping the number of global cells intact
  A technique to approximate area required for routing local nets and adjust the area of affected global cells
A complete graph model and IP formulation that
  Accounts for non-uniform global cells
  Includes vertex capacity in addition to edge capacity to address resource usage by local nets
  Accounts for other complicating factors that are supported by CGRIP
Integration with CGRIP
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 38: LCGRIP: Framework Overview
Binning Procedures
New graph and IP model with edge and vertex capacities
A framework to support new graph and new formulation
Detailed routing emulator
for validation
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 39: Binning Procedure
# of global nets: 2
# of local nets: 6
# of global cells: 9
# of global nets: 8
# of local nets: 0
# of global cells: 9
non-uniform
uniform
(a)
(b)
0 0 0 0 2
0
0
0
0
1
(d)
(e)
1 1 4 1 2
(c)
1
1
3
1
1
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 40: Local Congestion Balancing
0.0
0.0
0.125
0.125
0.0
0.0
0.375
0.0
0.0
0.375
0.0
0.0
0.0
0.0
0.0
0.0
0.125
0.125
0.125
0.0
average: 0.196
deviation: 3.26
0.0
0.1
0.1
0.1
0.1
0.0
0.33
0.0
0.0
0.33
0.0
0.0
0.0
0.0
0.0
0.0
0.125
0.125
0.125
0.0
(b) average: 0.160
deviation : 2.17
0.0
0.1
0.1
0.1
0.1
0.0
0.25
0.0
0.0
0.25
0.0
0.1
0.0
0.0
0.1
0.0
0.125
0.125
0.125
0.0
(c) average: 0.134
deviation: 1.67
0.0
0.1
0.1
0.1
0.1
0.0
0.25
0.0
0.0
0.25
0.0
0.125
0.0
0.0
0.125
0.0
0.1
0.1
0.1
0.0
(d) average: 0.130
deviation: 1.63
for gcell c
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 41: New Graph Model
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
C3
C1
C2
α0 α1 α2 α3=X
Β3= Y
β2
β1
β0
0
be
rv
The size of the grid graph does not change
The normalized edge capacities remain the same
  Corresponding to gcells of non-uniform size
Vertex capacity is introduced
  Based on approximation of routing resource usage of each local net
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 42: New Graph Model
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
C3
C1
C2
α0 α1 α2 α3=X
Β3= Y
β2
β1
β0
0
be
rv
To approximate resource usage by local nets
  Each local net is routed on its half-parameter bounding box on layers 2 and 3
  The area usage of each local net is computed considering its wire size
  Then summation of the areas of the local nets inside a gcell is subtracted from the gcell area
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 43: Example
16
24
24
24
24
6
6
6
6
4
4
4
4
6
6
6
6
24
24
24
24
16
edge capacity adjustment
edge and vertex capacity
Graph model without considering local congestion
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 44: IP-LC: An IP for Local Congestion
S1
T1
S2
T2
o10
s14
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 45: LCGRIP: Integration with CGRIP
2D Projection
  Similar to edge capacities, 2D vertex capacities are computed by adding their corresponding 3D vertex capacities
Reduced-sized linear programming (RLP)
  Based on formulation with vertex capacity (IP-LC)
Ripup and re-route (RRR)
  The shortest path algorithm considers both vertex and edge weights
Congestion-aware layer assignment (CLA)
  Wirelength minimization is based on gcells with non-uniform sizes
Introduction
Conclusions
CGRIP
LCGRIP
Summary
CGRIP
LCGRIP

## Slide 46: Simulation Setup
There is no detailed router that supports global routing solution
We implemented a detailed routing emulator for validation
  Visits the gcells sequentially
  Applies one iteration of RRR to route the nets inside each gcell
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
n2
n6
n7
n7
n6

## Slide 47: Simulation Setup
ISPD 2011 benchmarks
  Released as challenging benchmarks for routability
  Have large number of local nets when using the winning solutions from ISPD 2011 contest on routability-driven placement
Design | X x Y | # Nets | # 2T-Nets | %LC Uniform Non-uniform | 
superblue1 | 704x516 | 822744 | 2038444 | 30.8 | 14.1
superblue2 | 770x1114 | 990899 | 2237446 | 28.9 | 13.5
superblue4 | 467x415 | 567607 | 1316401 | 35.2 | 16.8
superblue5 | 774x713 | 786999 | 1713307 | 29.4 | 12.2
superblue10 | 638x968 | 1085737 | 2579974 | 34.1 | 34.0
superblue12 | 444x518 | 1293436 | 3480633 | 28.6 | 14.6
superblue15 | 399x495 | 1080409 | 2736271 | 34.4 | 15.8
superblue18 | 381x404 | 468918 | 1395388 | 28.2 | 15.0
average |  |  |  | 31.2% | 17.0%
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 48: Simulation Setup
Global Routing Variations
  U-E: Uniform grid with Edge capacity only
    It is identical to CGRIP
  U-AE: Uniform grid with Adjusted Edge capacity
    Similar to U-E but edge capacities are reduced based on the local nets in corresponding global cells
  U-AV: Uniform grid with Adjusted Vertex capacity
    Similar to U-E but we also consider vertex capacities
  NU-AV: Non-Uniform grid with Adjusted Vertex capacity
    Similar to U-AV but here the global cells are not uniform
NU-AV includes all the proposed features
Introduction
Conclusions
CGRIP
LCGRIP
Summary
6
6
6
6
4
4
4
4
6
6
6
6
24
24
24
24
16

## Slide 49: Simulation Setup
For each variation we allow our framework to run until there is no further overflow improvement
  Used as a congestion-aware global router that optimizes overflow as much as possible
Evaluation metrics
  GR-OF: overflow of GR with un-adjusted capacities
  DR-OF: total overflow computed by detailed routing emulator
  GR-T: runtime of global routing
  DR-T: runtime of detailed routing
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 50: Comparison of Evaluation Metrics
Design | U-E | U-AE | U-AV | NU-AV
superblue1 | 0 | 0 | 0 | 0
superblue2 | 3168 | 14496 | 10526 | 7756
superblue4 | 228 | 2024 | 880 | 420
superblue5 | 0 | 322 | 0 | 448
superblue10 | 124 | 4502 | 872 | 766
superblue12 | 0 | 274 | 302 | 12232
superblue15 | 0 | 1022 | 846 | 2582
superblue18 | 0 | 0 | 0 | 0
average | 1.0X | 6.4X | 3.8X | 6.9X
Design | U-E | U-AE | U-AV | NU-AV
superblue1 | 23142 | 23020 | 12740 | 806
superblue2 | 18880 | 18506 | 13154 | 9140
superblue4 | 28696 | 27476 | 13296 | 888
superblue5 | 10878 | 9256 | 2588 | 1032
superblue10 | 84842 | 73862 | 66780 | 65232
superblue12 | 44556 | 44416 | 36414 | 15566
superblue15 | 29982 | 29800 | 18886 | 7922
superblue18 | 11406 | 11184 | 558 | 444
average | 1.0x | 0.9x | 0.7x | 0.4x
GR-OF
DR-OF
The WL of U-AE, U-AV, NU-AV are up to 1% larger than U-E
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 51: Comparison of Runtime (minutes)
Design | U-E | U-AE | U-AV | NU-AV
superblue1 | 3 | 7 | 5 | 7
superblue2 | 352 | 321 | 303 | 381
superblue4 | 180 | 60 | 201 | 62
superblue5 | 135 | 184 | 164 | 220
superblue10 | 251 | 341 | 329 | 342
superblue12 | 238 | 360 | 309 | 302
superblue15 | 212 | 269 | 259 | 221
superblue18 | 10 | 20 | 16 | 10
average | 1.0X | 1.1X | 1.1X | 1.1X
Design | U-E | U-AE | U-AV | NU-AV
superblue1 | 28 | 21 | 18 | 7
superblue2 | 22 | 17 | 17 | 16
superblue4 | 39 | 25 | 25 | 10
superblue5 | 42 | 33 | 24 | 4
superblue10 | 62 | 51 | 32 | 33
superblue12 | 41 | 42 | 37 | 22
superblue15 | 34 | 24 | 19 | 11
superblue18 | 32 | 20 | 15 | 9
average | 1.0X | 0.8X | 0.6X | 0.4X
GR-T
DR-T
Introduction
Conclusions
CGRIP
LCGRIP
Summary
Increase in effort in GR results in decrease in effort in DR

## Slide 52: Conclusions
Proposed two techniques for considering local nets
  A technique for constructing non-uniform global cells that can decrease the number of local nets
  A new graph and IP model which include vertex capacity in addition to edge capacity
The framework accounts for other complicating factors
  Different wire size and spacing
  Virtual pins
  Routing blockages
Showed significant reduction in the detailed routing effort using our emulator
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 53: Summary of Contributions
Congestion prediction and reduction in modern designs
  H. Shojaei, A. Davoodi, J. T. Linderoth: Congestion analysis for global routing via integer programming. ICCAD 2011
  H. Shojaei, A. Davoodi, P. Ramanathan: Confidentiality preserving Integer Programming for Global Routing. To appear in DAC 2012*
  H. Shojaei, A. Davoodi, J. T. Linderoth: Planning for Local Net Congestion in Global Routing. Submitted to ICCAD 2012
  H. Shojaei, A. Davoodi, J. T. Linderoth: Congestion analysis for global routing via integer programming. Under progress, plan to submit to TCAD in May
  We made our framework available online at http://wiscad.ece.wisc.edu/gr/cgrip
  First version of CGRIP was used to judge the ISPD 2011 contest on routability-driven placement
  It was mentioned in EETimes as “gold standard in routability”
* This work proposes to use CGRIP in cloud in a secure mode
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 54: Summary of Contributions
Collaborative multi-objective global routing
  H. Shojaei, T. Wu, A. Davoodi, T. Basten: A Pareto-algebraic framework for signal power optimization in global routing. ISLPED 2010
  H. Shojaei, A. Davoodi, T. Basten: Collaborative Multi-objective global routing. Under revision in TVLSI
  H. Shojaei, A. H. Ghamarian, T. Basten, M. Geilen, S. Stuijk, R. Hoes: A parameterized compositional multi-dimensional multiple-choice knapsack heuristic for CMP run-time management. DAC 2009
Extended global routing ideas to FPGA
  N. Steiner, A. Wood, H. Shojaei, J. Couch, P. Athanas, M. French: Torc: towards an open-source tool flow. FPGA 2011
  N. Steiner, A. Wood, H. Shojaei, J. Couch, P. Athanas, M. French: TORC: Tools for Open Reconfigurable Computing. FCCM 2011
  Torc is hosted on http://torc-isi.sourceforge.net
Other contributions
  H. Shojaei, A. Davoodi: Trace signal selection to enhance timing and logic visibility in post-silicon validation. ICCAD 2010
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 55: Conclusions
Presented CGRIP as a fast congestion analysis framework that opens the doors to new research opportunities for routability improvement at early stages of the design flow like floorplanning and placement
Presented LCGRIP which optimizes congestion by treating global and detailed routing in a more holistic manner while modeling other factors contributing to congestion in modern designs
Presented Coll-MGR which provides a collaborative and multi-objective global routing framework to optimize several performance metrics simultaneously
  Presented in my prelim exam
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 56
Question?

## Slide 57
Backup Slides

## Slide 58: Overlapping Regions
We have [(rx-1)(ry-1)] regions that have overlap with other regions
The overlapping regions are defined by the red grid and start form Xr/2 and Yr/2
(c)
Xr
Yr
rx=6
ry=6
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 59: CGRIP: 2D Projection
Computing capacity of an edge in the projected 2D graph
  Compute , the normalized capacity for each edge on layer l from its capacity and add the 3D edge capacities corresponding to the same edge on the 2D projected grid-graph
  Example:
=
= 80,
= 20
= 80,
= 40
= 60
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 60: CGRIP: Blockages
Blockages are accounted for
  Blockages are the parts reserved for embedded IPs and memories
  The modern designs have irregular routing blockages
80 80 80 80 80 80
80 40 40 40 80 80
80 0 0 0 40 80
80 0 0 0 0 80
80 80 80 80 80 80
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 61: Congestion-aware Net Decomposition
Standard MST
Congestion-aware MST
3
4
3
12
4
12
10
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 62: Layer Assignment
Maze
Routing
Greedy
Approach
Introduction
Conclusions
CGRIP
LCGRIP
Summary
If an edge has overflow, the capacity of the corresponding edge on the lowest layer is adjusted:
For each edge the corresponding 3D edges are identified
  They are not blockages
  They are not used by other nets
We run maze routing on the identified edges
Maze routing may start from any layer to account for virtual pins
Notes: Hamid this is unclear. Do you have one 3 terminal net in this figure? Your sentence “Steiner point … are identified” is unclear

## Slide 63: Binning Procedure
# of global nets: 8
# of local nets: 0
# of global cells: 9
0 0 0 0 2
0
0
0
0
1
(b)
(c)
1 1 4 1 2
(a)
1
1
3
1
1
To control the increase in the number of local nets we consider a parameter η that determines the number of cut nets in each step
For each cut, it is moved to find a cut that results in closest value to
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 64: New Graph Model
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
C3
C1
C2
α0 α1 α2 α3=X
Β3= Y
β2
β1
β0
0
be
rv
Introduction
Conclusions
CGRIP
LCGRIP
Summary
approximate area for local net
approximate local resource used in
normalized vertex capacity:

## Slide 65: LCGRIP: Integration with CGRIP
Introduction
Conclusions
CGRIP
LCGRIP
Summary

## Slide 66: Detailed Routing Emulation
Works on a projected detailed routing
  one vertical and one horizontal layer
When there is a via, utilization of 1 unit is considered
n1
n1
n1
n2
n5
n2
n3
n3
n5
n5
n2
n6
n7
n7
n6
Introduction
Conclusions
CGRIP
LCGRIP
Summary